## Slide 1: CBE 333 - Adsorption
Adsorption Isotherms

## Slide 2: Sorption Background
Adsorption process:
  Solutes (aka sorbate) selectively transferred to insoluble solid surface (aka sorbent or resin)
Absorption process:
  Solutes selectively transferred into bulk of solid or liquid (aka absorbent)

## Slide 3: Adsorption
What binds solutes on the sorbent?
  Chemical bonds
  Weak molecular interactions
    Hydrophobic interactions
    Entropic effects
    Van Der Waals forces
  Electrostatic interactions
    + cations attracted to – anions
    Basis for ion exchange

## Slide 4: Adsorption and Ion Exchange

## Slide 5: Applications
Demineralization/deionization
  Water softening
Chromatography
  Analytical tool – identify compounds in mixture
  Processing – purify compounds, like proteins
Bulk filtration
  Removal of salt/vapors from gas with bone char
  Clarify water with charred wood

## Slide 6: Important Features
Capacity – how much solute the sorbent can adsorb
  Increases with surface area
  Porous materials attractive
  Lots of small pores better than a few big pores
Selectivity
Stability
  T, P, chemical contact
Regeneration/cleaning
Cost, availability, reproducibility
Good transport characteristics
  Low pressure drop across bed
  Quick adsorption/desorption possible
  Limited fouling
Ease of handling/packing into bed

## Slide 7: Adsorption of Liquid
Consider bulk liquid of known composition:
Different components
  interact with surface differently
  amount adsorbed varies
So surface composition is different than bulk composition

## Slide 8: Surface Area
Consider a spherical sorbent particle
Surface/Vol ↑ as r↓
Consider a cylindrical pore
Surface/Vol ↑ as dP↓

## Slide 9: Surface Area to Volume Ratio
Improves with small particles, small pores
  r ~ 50 mm to 1.2 cm
  dP < 20 Å to ~ 500 Å
Note: 10 Å = 1 nm = 10-9 m

## Slide 10: Bed Porosity: eb
Consider a packed bed of porous particles:
Vbed = Vparticles + Vvoids
mbed = mparticles
Bed density:
  rb = mparticles/Vbed
Particle density:
  rp = mparticles/Vparticles

## Slide 11: Particle Porosity: eP
Consider a porous particle:
Vparticle = Vsolid + Vpores
mparticle = msolid
Particle density:
  rP = msolid/Vparticle
True solid density or crystalline density:
  rS = msolid/Vsolid

## Slide 12: Specific Surface Area, Sg [m2/g]
Typical values of Sg ~ 300 to 1200 m2/g

## Slide 13: Equilibrium Considerations
Solute molecules moving between fluid (liq or gas) and solid surface
Dynamic equilibrium established
Need to relate fluid phase concentration to solute loading on the adsorbent
  Fluid concentration: xi, ci, etc.
  Solute loading: mass, moles or volume of solute per unit of surface area or unit of volume or unit of mass of the adsorbent

## Slide 14: Partitioning between fluid and solid
Few predictive tools
Rely on experimental data for adsorbate/adsorbent of interest
Measure adsorption isotherms showing:
Amount adsorbed versus amount in fluid phase at constant T

## Slide 15: Adsorption of Gas
Monolayer limited
Multilayer model
  (as in BET)
  DHads>DHcond
Convex multilayer
  undesirable
  DHads<DHcond
Multilayer with hysteresis
  filling vs emptying pores, or strong adsorption of impurities
Convex multilayer with hysteresis

## Slide 16: Liquid Adsorption
Binary mixture – solute & solvent
Generally assume
  Solvent does not adsorb
  D in composition of bulk liquid is due to adsorption of solute
Assumptions OK for dilute solutions
But give odd isotherms for concentrated systems

## Slide 17: Surface excess of solute, q1e
Assume solid attracts solute, decreasing the solute concentration of the bulk liquid
Let
  q1e = apparent moles of solute (1) adsorbed per unit mass of adsorbent
  n10 = moles of 1 in solution before solid added
  n1 = moles of 1 in bulk solution after solid added
  n0 = total moles of solution
  M = mass of adsorbent
  x10 =mole fraction of 1 in solution before solid added
  x1 = mole fraction of 1 in solution after solid added

## Slide 18: Typical Isotherms for Liquid Adsorption
q increases with c, similar to gas system; Seen if dilute solute in solvent that doesn’t adsorb or where adsorption is constant.

## Slide 19: Typical Isotherms for Liquid Adsorption
Seen if solvent not adsorbed; Initially solute adsorbed increases with concentration. But once the surface is saturated, increasing the moles in solution without increasing moles adsorbed lowers the surface excess.

## Slide 20: Typical Isotherms for Liquid Adsorption
Solvent adsorbs. Surface excess goes negative if amount of solute adsorbed isn’t high enough to compensate.

## Slide 21: Surface Excess Examples for nads = 100 moles
n0 moles | x10 | n1,ads moles | n2,ads = 100 - n1,ads moles | x1 | q1e
1000 | 0.5 | 10 | 90 | 490/900= 0.54 | <0
1000 | 0.5 | 50 | 50 | 450/900 = 0.5 | =0
1000 | 0.5 | 90 | 10 | 410/900= 0.46 | >0

## Slide 22: Modeling Liquid Adsorption
Familiar models
  Henry’s Law
  Langmuir
  Freundlich
OK for limited range of conditions
qi = kiCi

## Slide 23: Adsorption Isotherm Experiments
Obtain isotherms for 2 proteins
  Bovine Serum Albumin (BSA), Hemoglobin (Hb)
On 4 resins
  Cation exchange (negative binding sites)
    Toyopearl SP-650S (35 μm), Toyopearl CM-650S (35 μm)
  Anion exchange (positive binding sites)
    Toyopearl Super Q-650S (35 μm), Toyopearl DEAE-650S (35 μm)
In buffers of 2 different pH values
  pH = 4.7 or 8
At 2 temperatures
  25 °C, 35 °C

## Slide 24: Adsorption Isotherm Experiments
Each team collects data for 4 isotherms
→ Hb and BSA at 25 °C and 35 °C
Pools data with team from the other sections.
→ 4 different resins
Plots adsorption isotherms for 16 conditions, and fits each data set with a Langmuir model.
Compares Qmax and K values.
Identifies best system for separating mixtures of BSA & Hb.