## Slide 1: CBE 333 - Distillation
Exploiting differences in volatilities.
Key Concepts:
Material & Energy Balances
Vapor-Liquid Equilibrium

## Slide 2: Distillation Overview
Separation by phase creation
  2 phases – liquid and vapor
  More volatile components enrich vapor
  Less volatile components enrich liquid
Advantages:
  Well-developed technology
  Can produce high purity product(s)
  No new mass separating agent to remove
Disadvantages:
  Energy intensive
  Costly

## Slide 3: Distillation Column
Figure 7.2, Seader et al, Separation Process Principles, 3rd ed., John Wiley & Sons, New York (2011)
Equipment:
Column
Condenser – total vs. partial
Reboiler – total vs. partial
Streams:
In: Feed (F)
Out: Distillate (D) & Bottoms (B)
Reflux (L)
Boilup (V’)

## Slide 4: Series of Equilibrium Stages
Figure 5.12 (c), Seader et al, Separation Process Principles, 3rd ed., John Wiley & Sons, New York (2011)
Each stage (n) is at equilibrium:
TV,n = TL,n = Tn
PV,n = PL,n = Pn
μi,Vn = μ i,Ln = μi,n
Basic Idea:
More volatile components increase in V,
and Vn fed to stage above
Less volatile components increase in L,
and Ln fed to stage below
Separation of components amplified by series of equilibrium stages

## Slide 5: Equilibrium Stage:
Ln and Vn produced at each stage are in equilibrium:
Ln+1 and Vn-1 fed to stage and Ln and Vn produced at the stage are linked by SS material balances:
Vn-1
yi,n-1
Ln
xi,n
Vn
yi,n
Ln+1
xi,n+1

## Slide 6: Our Distillation Experiment
Our Column:
6 trays
Partial reboiler
Total condenser
Total of 7 stages
We select:
Feed tray location
Reflux ratio

## Slide 7: Feed Tray Location
Above feed tray
Rectification or enriching section
Vapor is enriched with more volatile components
Below feed tray
Stripping section
Liquid is depleted of more volatile components
Feed tray belongs to both sections

## Slide 8: Reflux versus Reflux Ratio
V = L + D
Distillate (D) = liquid product from the top
Reflux (L) = liquid returned to the column
Reflux ratio (R) = ratio of reflux flow rate to distillate flow rate

## Slide 9: Values of R
As L → 0, R → 0
  Lots of distillate!
  No liquid flow to top of column
  No absorption of less volatile species by liquid
As D → 0, R → ∞
  Lots of liquid flow in top of column
  Good removal of less volatile species
  No product!
Good operation: R ~ 1.1 to 1.5 x Rmin

## Slide 10: Distillation Column: Material Balances on Top of Column
SS total material balance over top of column to nth plate:
SS material balance on solute over top of column to nth plate:
Solve for yn+1:
Counting plates from top:

## Slide 11: Constant Molar Overflow Assumption
Constant flow of liquid and vapor if:
  ΔHA,vap≈ ΔHB,vap ≈ constant
  and ΔHmix << ΔHi,vap
  Q ≈ 0 (OK for a well-insulated column)
  P ≈ constant

## Slide 12: Operating Line for Top of Column
With the constant molar overflow assumption:
Generates line linking yn+1 and xn
Slope:
Intercept:

## Slide 13: Distillation Column: Material Balances on Bottom of Column
SS total material balance over bottom of column to mth plate:
SS material balance on solute over bottom of column to mth plate:
Solve for ym:
Counting plates from bottom:

## Slide 14: Operating Line for Bottom of Column
With the constant molar overflow assumption:
Where VB is the boil-up ratio defined by
Analogous to reflux ratio. Both a ratios of flow rate of material returned to column to flow rate of product withdrawn.

## Slide 15: McCabe Thiele Diagram
Graphical method showing
  # of stages
  Stream compositions
  Operating conditions
Allows determination of
  Number of theoretical trays, Nt
  Minimum Number of theoretical trays, Nt,min
  Minimum reflux ratio, Rmin
  Optimal feed tray location

## Slide 16: Construction of a McCabe-Thiele Diagram
Consider a binary system, where species 1 is the more volatile component
x = mole fraction of species 1 in the liquid phase
y = mole fraction of species 1 in the vapor phase

## Slide 17: Distillation Requires VLE
Workable operating conditions set by thermo!
If column P is fixed, need Tbub<T<Tdew

## Slide 18: Construction of a McCabe-Thiele Diagram
McCabe-Thiele Diagram is an xy diagram with 5 parts:
  45° reference line, y = x
  Vapor-liquid equilibrium curve, y = Kx
  Known concentrations of streams (xF, xB, xD) or trays (x1,x2…xn)
  q line, depicting phase or thermal condition of the feed
  Two operating lines
    (top section of column, and bottom section of column)
  Recognize that the Feed Tray is part of both the top and the bottom of the column. So feed line and both operating lines must intersect at a common point!

## Slide 19: Example

## Slide 20: q-line
Depicts composition and quality of feed
Feed is some combination of liquid and vapor
  Material balance:
      FzA = VyA + LxA
      zA = (V/F) yA + (F-V)/F xA = V yA + (1- V )xA
      Where V = fraction vapor
  Rearrange to get q-line:
      yA = (V - 1)/V xA + 1/V zA
      yA = q/(q – 1) xA – 1/(q-1) zA
      Where q = 1-V = fraction liquid

## Slide 21: q-line and Flows at the Feed Tray
State of Feed:
Sub-cooled liquid
Saturated liquid
L-V mixture
Saturated vapor
Superheated vapor
At Feed Tray:

## Slide 22: q – line slope = q/(q-1)

## Slide 23: Finding Nt,min for a specified xD, xB
Fewer trays needed as R increases
Minimum trays found at max R, and max value seen when D = 0 and R = ∞
As R → ∞:
  slopes of top and bottom op lines → 1
  Converge on the 45° reference line
As R decreases:
  Intersection of q-line and op lines moves closer to VLE curve
  Separation per step drops
  Number of trays required increases

## Slide 24: Finding Nt,min for a specified xD, xB
Step off between 45° reference line and VLE curve to get Nt,min

## Slide 25: Finding Rmin
The intersection of the feed line and the 2 operating lines must be between the reference line and the VLE curve.
All points on the operating lines must be between the reference line and the VLE curve.
If an operating line intersects the VLE curve, an infinite number of stages is required!

## Slide 26: Finding Rmin

## Slide 27: Finding Optimal Feed Tray Location for a Specific R Value
  Construct McCabe-Thiele Diagram
  Reference line
  VLE curve
  Known concentrations
  q line
  Two op lines
  Step off trays from the top
  Switch from top op to btm op as soon as the stage with the feed line has vapor on top op and liquid on btm op

## Slide 28: Finding Nt when R and Feed Tray Location is Specified
Just right
  Nt = 5
Left: feed too low
  Nt ↑ to 7
Right: feed too high
  Nt ↑ to 6

## Slide 29: What if VLE isn’t achieved?
Can incorporate Murphree Vapor Efficiency with modified VLE curve

## Slide 30: What if the reflux is subcooled?
Subcooled reflux:
Cold reflux condenses some of V before it leaves the column
So real reflux ratio in column > L/D
  Beneficial!
  McCabe-Thiele still works, but use real R for slope of top operating line
Real reflux ratio:

## Slide 31: Tray Efficiency
Eo experimental = Nt/Nact
Drickamar and Bradford correlation:
Equation 7-42, Seader et al, Separation Process Principles, 3rd ed., John Wiley & Sons, New York (2011).
  Eo = 13.3 – 66.8log(mL[cP])
Murphree Tray Efficiency

## Slide 32: Our Experiment
Separating a mixture of isopropanol/water
Looking at separation factor
Pooling data between teams & sections
  Effect of reflux ratio?
  Effect of saturated/superheated/subcooled feed?
  Effect of saturated/subcooled reflux?